## Slide 1: Signal

## Slide 2: Ohm’s law
V = Voltage in volts
I = Current in amps
R = Resistance in ohms

## Slide 6: Analog vs digital
Infinite  analog
Finite  digital

## Slide 9: analogRead()
BOARD | OPERATING VOLTAGE | USABLE PINS | MAX RESOLUTION
Uno | 5 Volts | A0 to A5 | 10 bits
Mini, Nano | 5 Volts | A0 to A7 | 10 bits
Mega, Mega2560, MegaADK | 5 Volts | A0 to A14 | 10 bits
NodeMCU | 3.3 Volts | A0 | 10 bits

## Slide 10: analogWrite()

## Slide 11: Voltage divider
turns a large voltage into a smaller one

## Slide 14: Potentiometers

## Slide 15: Resistive sensors
Photocell
Light Level | R2 (Sensor) | R1 (Fixed) | Ratio R2/(R1+R2) | Vout
Light | 1kΩ | 5.6kΩ | 0.15 | 0.76 V
Dim | 7kΩ | 5.6kΩ | 0.56 | 2.78 V
Dark | 10kΩ | 5.6kΩ | 0.67 | 3.21 V

## Slide 16: Analog to digital converter (ADC)

## Slide 17: UNO

## Slide 18: Sampling rate
Frequency of sampling
22,050 Hz
Distance = 1 / 22,050 second = 45.35 µs

## Slide 21: Dilemma
the higher the sampling rate –, the more perfect will be the analog signal produced by the digital-to-analog converter (DAC)
the more samples we capture more storage space is necessary to store the resulting digital data